Correlation Coefficient Code in C++ for K0TO

This code calculates the correlation coefficient between a given array of data and a reference peak. It consists of a header file, corrcoef.h, to be included in another C++ program. For convenience, the header file is complete - it includes the function definitions, and no special steps need to be taken to compile code with this file.
corrcoef.h includes a single class, corrcoef. It has a constructor (and destructor), and a function analyze, which actually calculates the correlation coefficients. It also has a number of public variables to input parameters and retrieve data from the algorithm.
First, instantiate a corrcoef object. The constructor takes a single integer: the size of the data array. The parameter variables will be initialized to their default values. These parameters may be accessed directly. Then, call the analyze function, passing a pointer to the (integer) data array, as well as the number of elements in the array. The calculated values will be stored in the four output arrays.

Input Parameters
Set these to desired values after instantiating and before running analyze on any data.

int corrcoeff.kstart
Default: 0
The correlation coefficients will be calculated beginning at this value. If the earliest the peak is expected to begin at is 20, for instance, this could be set to 20, to reduce the number of coefficients that are calculated.

int corrcoeff.kend
Default: 63 (see constructor)
The correlation coefficients will be calculated until this value. When the start of the reference peak shifts to this value, the function will return. Therefore, in combination with kstart, a window may be defined such that the correlation coefficients will only be calculated in the range of this window.

int corrcoeff.threshold
Default: 0
Minimum value of the square of the correlation coefficient for it to be recorded.

int corrcoeff.minarea
Default: 0
The sum of the 21 samples being compared against the reference peak must exceed this value for the correlation coefficient to be calculated.

Output
After analyze is called, these variables will contain the output of the algorithm.

int corrcoeff.numary
The number of correlation coefficients that were recorded. The following arrays have data in elements zero through numary.

int* corrcoeff.locary
Pointer to an array containing the starting sample position of the data correlated against for output values at this index. In other words, if at element 5 of this array, the value 29 is stored, then each of the following arrays hold at element 5 output corresponding to the 21 samples beginning at sample 29.

int* corrcoeff.arary
An array containing the sum of the 21 consecutive samples compared against the reference peak for each position where a correlation coefficient was recorded.

double* corrcoeff.ccary
An array containing the actual, calculated correlation coefficients.

double* corrcoeff.timary
The time at which the peak occurs is stored in this array. It is calculated according to a weighted average.

double* corrcoeff.timsqary
Mean square width of the 21 channels. (Square of the RMS value)

Functions

corrcoeff::corrcoeff(int size)
Constructor. It initializes the input parameters to their default values. The output arrays listed above are allocated with a number of elements equal to the passed parameter size. It should ordinarily be set equal to the number of samples of data that will be passed to each call of analyze.

void corrcoeff::analyze(int* stream, int samples)
Performs the correlation coefficient algorithm. The data to be analyzed are stored in an array pointed to by stream. It should meet the following criteria:
-Data are pedestal subtracted
-Eight samples of zeroes are inserted at the beginning and end of the data.
The parameter samples is the size of the array pointed to by stream. After analyze is called, the output variables listed above will be filled with data that can be extracted.

Example Code
Included is a simple program test.cpp that will take in a pedestal and 64 samples of data from the standard input and perform analysis on them. The results will be put in standard output. Recall that in Bash, a file may be taken as the standard input to a program using <. For instance, the following will display the output from processing the data in the included testdata1 file:

./test < testdata1